## Slide 1
Sevde Zümrüt İspay
Melis Karakurt
Burak Kurt
Güner Şirin
Levent Kandiller
Simge Güçlükol Ergin
A WAREHOUSE MANAGEMENT DECISION SUPPORT SYSTEM FOR TOTOMAK
İrem Amaç
Doğuş Özbaş

## Slide 2: CONTENTS
  System Analysis (Micro/Macro)
    Problem Definition
Modeling Approach and Solution Methodology
Decision Support System (DSS)
Conclusion
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 3: SYSTEM ANALYSIS
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 4
            Totomak was founded in 1950
            Machinery and spare parts company in Çiğli İzmir
            95% of Sales  Export
            Total Floor Area : 17,500 m2 (10,000 m2 closed)
            Sales Revenue : 51 m EUR (2021), 63 m EUR (2022)
            Manpower: 550 employees
              Precision Machining: Job Shop
            Assembly & Test: Flow Shop
            Design: Lean Prototyping & Co-design
            Manufacturing System
              Production Processes
              Assembly and Test Lines
            Customer Sector Distribution & Global Presence
              Automative 16%
              Climatization 50%
              Heavy Duty Machining 30%
              Energy 4%
SYSTEM ANALYSIS
MACRO
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 5
            Collected Data
2021
2022
SYSTEM ANALYSIS
MICRO
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
            ABC (Pareto) Analysis
Part Number | 12.05.2023 | 19.05.2023 | 26.05.2023 | 2.06.2023 | Other Weeks
X1 | 24 | 11 | 8 | 9 | . . .
X2 | 12 | 47 | 24 |  | . . .
X3 | 24 | 12 | 36 | 12 | . . .
X4 | 35 | 20 |  | 42 | . . .
X5 | 9 | 24 | 55 | 48 | . . .
X6 | 11 |  | 14 | 5 | . . .
X7 |  |  | 78 |  | . . .
. . | . . | . . | . . | . . | 
2023

## Slide 6
SYSTEM ANALYSIS
MICRO
Starting Point
A
B
Distance between A and B is 18m
            a New Warehouse Layout
            LayoutDistance Matrix (1320 locations)

## Slide 7: PROBLEM DEFINITION
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 8
Random use of locations
Work safety problems
Pick and place operations
are not scheduled
Some required data are not collected
Collected data are either not stored in an easy format or not accessable
Fishbone Diagram
Data accessibility for analysis
Pick and place operations
No policy for picking like FIFO
Manual Routing by the forklift operator
Random entry and exit of the products
It may cause the products to be kept in inventory for a long time and become deformed
Chaotic
warehouse
management!
Unknown SKU locations
SKU locations are not monitored
Not easy access to products
Redundant forklift movement
Extra transport time
PROBLEM DEFINITION
Symptoms
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 9: LITERATURE REVIEW
Warehouse
Ratliff. H. D.. & Rosenthal. A. S. (1983). Order-picking in a rectangular warehouse: a solvable case of the traveling salesman problem. Operations research. 31(3). 507-521.
Petersen. C. G.. & Schmenner. R. W. (1999). An evaluation of routing and volume‐based storage policies in an order picking operation. Decision Sciences. 30(2). 481-501.
Caron. F.. Marchet. G.. & Perego. A. (2000). Optimal layout in low-level picker-to-part systems. International Journal of Production Research. 38(1). 101-117.
Petersen. C. G.. & Aase. G. (2004). A comparison of picking. storage. and routing policies in manual order picking. International journal of production economics. 92(1). 11-19.
ABC Analysis (Pareto)
Douissa. M. R.. & Jabeur. K. (2016). A new model for multi-criteria ABC inventory classification: PROAFTN method. Procedia Computer Science. 96. 550-559
Nyman. D.. & Levitt. J. (2001). Maintenance planning. scheduling. and coordination. Industrial Press Inc.
Pareto. V. (1971). Manual of political economy.
Ng. W. L. (2007). A simple classifier for multiple criteria ABC analysis. European Journal of Operational Research. 177(1). 344-353.
Bragg. S. M. (2013). Inventory management. Colorado: Accounting Tools.
Assignment Problem
Thompson. G. L. (1981). A recursive method for solving assignment problems. In North-Holland Mathematics Studies (Vol. 59. pp. 319-343). North-Holland.
Konig. D. (1931). Graphok es matrixok [in Hungarian: Graphs and matrices]. Mat es Fizikai Lapok 38. 116-119.
Jacobi. C. G. (1890). De aequationum differentialum systemate non normali ad formam normalem revocando. . Vorlesungen über Dynamik von C. G. J. Jacobi nebstes fünf hinterlassenen Abhandlungen desselben . herausegegeben von A. Clesch. Berlin. Druck und Verlag von Georg Reimer. 1866. p. 550–578 et C.G.J. Jacobi's gesammelte Werke. fünfter Band. herausgegeben von K. Weierstrass. Berlin. Druck und Verlag von Georg Reimer. 1890. p. 485-513. (cf[I/67 a) et b)])
Quadratic Assignment Problem
Li. W. J.. & Smith. J. M. (1995). An algorithm for quadratic assignment problems. European Journal of Operational Research. 81(1). 205-216.
Sahni. S.. & Gonzalez. T. (1976). P-complete approximation problems. Journal of the ACM (JACM). 23(3). 555-565.
Koopmans. T. C.. & Beckmann. M. (1957). Assignment problems and the location of economic activities. Econometrica: journal of the Econometric Society. 53-76.
Ji. P.. Lee. W. B.. & Li. H. (1997). A new algorithm for the assignment problem: An alternative to the Hungarian method. Computers & operations research. 24(11). 1017-1023
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 10: MODELING APPROACH AND SOLUTION METHODS
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 11: Our Approach
Mathematical Modelling Based Decisions
  Tactical Level: Shelf Allocation for 6 months based on sales data
  Operational Level: Optimizing Forklift pick/place operations per day
MODEL 1
MODEL 2
  Tactical Level: Minimize total handling duration  shelf allocation: 6 months based on sales data + ABC
  Operational Level: Minimize #Forklift sorties and total distance travelled for daily pick/place operations
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 12
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
 | Demand: Weeks (Number Of Products) |  |  |  |  |  | 
Item | Week 1 | Week 2 | Week 3 | Week 4 | Week 5 | … | Week 26
X2 | 12 | 24 | 48 | 6 | 72 | … | 25
X3 | 48 | 12 | 36 | 60 | 84 | … | 43
X4 | 20 | 32 | 44 | 8 | 4 | … | 15
Item | #products/pallet
X2 | 6
X3 | 12
X4 | 4
 | Demand: Weeks (Number of Pallets) |  |  |  |  |  | 
Item | Week 1 | Week 2 | Week 3 | Week 4 | Week 5 | … | Week 26
X2 | 2 | 4 | 8 | 1 | 12 | … | 20
X3 | 4 | 1 | 3 | 5 | 7 | … | 24
X4 | 5 | 8 | 11 | 2 | 1 | … | 18
Item | Max Weekly Demand | Safety Stock | Max ATP | Total Demand | Turnover
X2 | 12 | 3 | 15 | 27 | 1.8
X3 | 7 | 2 | 9 | 20 | 2.2
X4 | 11 | 3 | 14 | 27 | 1.9
MODELING APPROACH & SOLUTION METHODS
Creating Parameters of Model 1
Production Lead time is one week!

## Slide 13
            Medium term (6 months or 1 year) demand  max ATP  required allocation  ( many locations
            Each pallet can be placed on only one location
            Each location can have only one pallet
Model 1
            = The distance between the base and the locations wrt forklift movements
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
MODELING APPROACH & SOLUTION METHODS
The distance between
forklift and locations is

## Slide 14
Sets. Parameters and Decision Variables of Model 1
Decision Variable:
= SKU to be reserved on location
Parameters:
= Frequency of turnover
= d for SKU's
= Distance between the base and the locations wrt forklift movements
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
Set:
s = Stock Keeping Unit and s∈S={1,2.…...|S|}
MODELING APPROACH & SOLUTION METHODS

## Slide 15
            (1): The objective function optimizes the shelf locations of goods while minimizing the total distance required for forklift operations
            (2): Shelf allocation
            (3): At most one pallet per location
            (4): Defines the range of decision variables
Model 1
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
∈{0,1} (4)
MODELING APPROACH & SOLUTION METHODS

## Slide 16
Transformation to an Assignment Problem
TURNOVER | ITEM | SHELF NUMBER | 1 | 2 | 3 | 4 | 5
3.15789474 | X2 | 1 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 2 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 3 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 4 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 5 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 6 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 7 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 8 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 9 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 10 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
3.15789474 | X2 | 11 | 205.263158 | 200.842105 | 196.421053 | 192 | 187.578947
DISTANCE | 65 | 63.6 | 62.2 | 60.8 | 59.4
. .
. .
. .
. .
. .
. .
. .
. .
0.0001 | DUMMY | 1320 | 0.0065 | 0.00636 | 0.00622 | 0.00608 | 0.00594
102.1
. .
1320
322.421053
322.421053
322.421053
322.421053
322.421053
322.421053
322.421053
322.421053
322.421053
322.421053
322.421053
0.01021
. .
. .
. .
. .
. .
. .
. .
. .
. .
. .
. .
. .
. .
. .
MODELING APPROACH & SOLUTION METHODS

## Slide 17: Heuristic
Items are sorted in descending order by the calculated turnover values.
And sorted items are cloned as many as their ATP values.
Then locations are sorted in ascending order.
Final step was matching the minimum distance with the cloned item which has maximum turnover.

## Slide 18
Comparison of Methods for Model 1
MODEL 1 |  |  |  |  |  |  |  | 
OBJECTIVE FUNCTION | OBJECTIVE FUNCTION |  |  |  | TIME(CPU sec) | TIME(CPU sec) |  | 
PROBLEM | GPS | Hungarian | Heuristic | %GAP(H) | PROBLEM | GPS | Hungarian | Heuristic
1 | 4290.10 | 4290.10 | 4589.62 | 6.98% | 1 | 0.00235 | 0.00023 | 0.00171
2 | 11566.44 | 11566.44 | 12464.99 | 7.77% | 2 | 0.00211 | 0.00019 | 0.00179
3 | 7276.34 | 7276.30 | 7875.37 | 8.23% | 3 | 0.00017 | 0.00025 | 0.00131
4 | 4942.04 | 4942.04 | 5241.56 | 6.06% | 4 | 0.00268 | 0.00019 | 0.00156
5 | 16235.03 | 16235.03 | 17732.61 | 9.22% | 5 | 0.00267 | 0.00021 | 0.00131
6 | 5593.98 | 5593.98 | 5893.50 | 5.35% | 6 | 0.00224 | 0.00024 | 0.00176
7 | 12596.86 | 12596.86 | 13794.92 | 9.51% | 7 | 0.00178 | 0.00024 | 0.00155
8 | 14552.68 | 14552.68 | 15750.74 | 8.23% | 8 | 0.00121 | 0.00030 | 0.00189
9 | 19494.72 | 19494.72 | 20992.29 | 7.68% | 9 | 0.00317 | 0.00021 | 0.00162
10 | 19873.20 | 19873.20 | 21670.29 | 9.04% | 10 | 0.00264 | 0.00023 | 0.00161
 |  |  |  | 7.81% | Average | 0.00210 | 0.00023 | 0.00161
 |  |  |  | 9.51% | Worst | 0.00317 | 0.00030 | 0.00189
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
MODELING APPROACH & SOLUTION METHODS
            All codes were executed on Acer nitro i7 9th generation 16gb ram and based on the conducted experiments, pandas, scipy, numpy libraries are used in python code.
            Toy instances: 10 item 100 locations.

## Slide 19: Our Approach
Mathematical Modelling Based Decisions
  Tactical Level: Shelf Allocation for 6 months based on sales data
  Operational Level: Optimizing Forklift pick/place operations per day
MODEL 1
MODEL 2
  Tactical Level: Minimize total handling duration  shelf allocation: 6 months based on sales data + ABC
  Operational Level: Minimize #Forklift sorties and total distance travelled for daily pick/place operations
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 20: MODELING APPROACH
Sets. Parameters and Decision Variables of Model 2
Parameters:
= Distance between forklift and locations
= Distance of location of the item i
= Distance between the starting point and placing product j
= Distance between the picking product i and turning to the starting point
= Distance between picking and placing
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
Sets:
s = Stock Keeping Unit and s∈S={1,2.…...|S|}
k = Number of sorties and k∈K={1,2... . |K|}
Decision Variables:
=
=

## Slide 21
            (1): Minimizes the number of sorties that must be done
            (7): Ensures that the minimum number of sorties is made
(2): Minimizes the distance and time forklifts will take to pick and place the product
(3): Guarantees that at most one product will be picked for every sortie
            (4): Guarantees that at most one product will be placed for every sortie
            (5): Prevents redundant picking sortie to be done
(6): Prevents redundant placing sortie to be done
            (8): Defines the range of decision variables
MODELING APPROACH
Model 2.1: QUADRATIC ASSIGNMENT
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 22
            (1): Minimizes the number of sorties that must be done
            (7): Ensures that the minimum number of sorties is made
(2): Minimizes the distance and time forklifts will take to pick and place the product
(3): Guarantees that at most one product will be picked for every sortie
            (4): Guarantees that at most one product will be placed for every sortie
            (5): Prevents redundant picking sortie to be done
(6): Prevents redundant placing sortie to be done
            (8): Defines the range of decision variables
MODELING APPROACH
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
Model 2.1: QUADRATIC ASSIGNMENT

## Slide 23
            This model is about daily forklift operation optimization.
            Only one product will be picked and placed.
            In order to minimize the number of sorties, each product will be assigned to a sortie.
Model 2
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
MODELING APPROACH & SOLUTION METHODS

## Slide 24
            If we assign products to each other, not to sorties, the problem becomes linearized and becomes an assignment problem
            (1): Minimizes the distance that forklifts will take to pick and place the products.
            (2): Guarantees that a product will be picked for every sortie.
MODELING APPROACH
Model 2.2: LINEAR ASSIGNMENT
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
            (3): Guarantees that a product will be placed for every sortie.
            (4): Range of the decision variable
Constant Distance

## Slide 25
Instance Generation: 10 pick + 10 place  20 toy instances
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
PICKED | FULL CELLS RESERVED FOR ITEM |  |  | SHELVES REZERVED FOR ITEM | 
X62 | 44 | 33 | 43 |  | 
X120 | 174 | 25 | 127 | 173 | 
X65 | 249 | 304 |  |  | 
X185 | 303 | 155 | 293 | 339 | 257
X110 | 384 | 256 | 292 | 200 | 246
. . | . . | . . | . . | . . | . .
PLACED | EMPTY CELLS RESERVED FOR ITEMS |  |  | SHELVES REZERVED FOR ITEM | 
X45 | 84 | 88 | 130 | 75 | 
X61 | 164 | 72 | 36 |  | 
X146 | 23 | 69 | 124 | 159 | 217
X71 | 300 | 254 | 382 | 336 | 428
X188 | 379 | 471 |  |  | 
. . | . . | . . | . . | . . | . .
75
72
159
254
379
. .
RANDOMLY SELECTED CELLS LOCATION FOR PLACING
PLACED
X45
X61
X146
X71
X188
. .
Randomly
SELECTED SHELF LOCATION FOR PICKING
44
127
249
257
384
. .
PICKED
X62
X120
X65
X185
X110
. .
According to FIFO
 | 44 | 127 | 249 | 257 | 384
75 | 63 | 98.35 | 127.75 | 133.7 | 183.4
72 | 48.857 | 76.271 | 99.071 | 103.69 | 142.23
159 | 56.842 | 88.737 | 115.26 | 120.63 | 165.47
254 | 18 | 28.1 | 36.5 | 38.2 | 52.4
379 | 65.25 | 101.86 | 132.31 | 138.48 | 189.95
SOLUTION METHODS
According to FIFO

## Slide 26: Heuristic
 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7 | Y8 | Y9 | Y10
X1 | 19.3333333 | 14 | 8.66666667 | 7.33333333 | 5.33333333 | 6.66666667 | 20 | 16 | 10 | 9.33333333
X2 | 2 | 4.66666667 | 8.66666667 | 18 | 12 | 10.6666667 | 2.66666667 | 2.66666667 | 7.33333333 | 8
X3 | 2.66666667 | 2.66666667 | 8 | 17.3333333 | 11.3333333 | 10 | 3.33333333 | 0.66666667 | 6.66666667 | 7.33333333
X4 | 13.3333333 | 8 | 2.66666667 | 6.66666667 | 3.33333333 | 0.66666667 | 14 | 10 | 8 | 3.33333333
X5 | 15.3333333 | 10 | 7.33333333 | 4.66666667 | 2.66666667 | 5.33333333 | 16 | 12 | 14 | 6.66666667
X6 | 24 | 18.6666667 | 14.6666667 | 8 | 10 | 12.6666667 | 24.6666667 | 20.6666667 | 21.3333333 | 14
X7 | 9.33333333 | 4 | 1.33333333 | 10.6666667 | 4.66666667 | 3.33333333 | 10 | 6 | 8 | 0.66666667
X8 | 16 | 13.3333333 | 10.6666667 | 4 | 6 | 8.66666667 | 16.6666667 | 15.3333333 | 17.3333333 | 10
X9 | 15.3333333 | 10 | 7.33333333 | 4.66666667 | 2.66666667 | 5.33333333 | 16 | 12 | 14 | 6.66666667
X10 | 23.3333333 | 18 | 12.6666667 | 3.33333333 | 9.33333333 | 10.6666667 | 24 | 20 | 14 | 13.3333333

## Slide 27
SOLUTION METHODS
Comparison of Methods for Model 2
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
MODEL 2 |  |  |  |  |  |  |  | 
OBJECTIVE FUNCTION |  |  |  | TIME |  |  |  | 
PROBLEM | GPS | Hungarian | Heuristic | %GAP(H) | PROBLEM | GPS | Hungarian | Heuristic
1 | 61.33 | 61.33 | 65.33 | 6.58% | 1 | 0.0522 | 0.0087 | 0.0002
2 | 128.66 | 128.66 | 154.00 | 19.70% | 2 | 0.0109 | 0.0043 | 0.0002
3 | 88.66 | 88.66 | 106.00 | 19.64% | 3 | 0.0144 | 0.0032 | 0.0001
4 | 149.33 | 149.33 | 185.33 | 24.11% | 4 | 0.0183 | 0.0024 | 0.0003
5 | 108.66 | 108.66 | 108.67 | 0.01% | 5 | 0.0162 | 0.0035 | 0.0001
6 | 115.33 | 115.33 | 122.00 | 5.78% | 6 | 0.0223 | 0.0013 | 0.0002
7 | 82.66 | 82.66 | 84.00 | 1.62% | 7 | 0.0209 | 0.0077 | 0.0005
8 | 274.66 | 274.66 | 313.33 | 14.08% | 8 | 0.0135 | 0.0041 | 0.0001
9 | 95.33 | 95.33 | 99.33 | 4.20% | 9 | 0.0143 | 0.0076 | 0.0002
10 | 85.33 | 85.33 | 108.00 | 26.57% | 10 | 0.0301 | 0.0059 | 0.0002
11 | 148.00 | 148.00 | 172.00 | 16.22% | 11 | 0.0134 | 0.0082 | 0.0004
12 | 113.33 | 113.33 | 133.33 | 17.65% | 12 | 0.0194 | 0.0016 | 0.0002
13 | 113.33 | 113.33 | 120.00 | 5.89% | 13 | 0.0111 | 0.0028 | 0.0002
14 | 108.00 | 108.00 | 108.00 | 0.00% | 14 | 0.0186 | 0.0097 | 0.0002
15 | 68.00 | 68.00 | 69.33 | 1.96% | 15 | 0.0153 | 0.0044 | 0.0002
16 | 175.33 | 175.33 | 195.33 | 11.41% | 16 | 0.0125 | 0.0079 | 0.0002
17 | 165.33 | 165.33 | 178.67 | 8.07% | 17 | 0.0175 | 0.0077 | 0.0006
18 | 103.33 | 103.33 | 142.00 | 37.42% | 18 | 0.014 | 0.0065 | 0.0002
19 | 106.00 | 106.00 | 130.00 | 22.64% | 19 | 0.0137 | 0.0071 | 0.0002
20 | 93.33 | 93.33 | 110.67 | 18.58% | 20 | 0.0100 | 0.0016 | 0.0002
 |  |  |  | 13.11% | Average | 0.0179 | 0.0053 | 0.0003
 |  |  |  | 37.42% | Worst | 0.0522 | 0.0097 | 0.0006
            All codes were executed on Acer nitro i7 9th generation 16gb ram and based on the conducted experiments, pandas, scipy,numpy libraries are used in python code.
            Toy instances: 10 item 100 locations.

## Slide 28: DECISION SUPPORT SYSTEM
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 29
DECISION SUPPORT SYSTEM
Place the items
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 30
DECISION SUPPORT SYSTEM
See the best sortie of the picked and placed items of the day
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 31
Model Base
Verification and Validation of the DSS: ᷉ 25 pick+25 place
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
 | TOTOMAK'S TOUR (m) | OUR TOUR (m) | DIFFERENCE | EFFICIENCY
DAY 1 | 6397 | 5123 | 1274 | 19.92%
DAY 2 | 6167 | 4981 | 1186 | 19.23%
DAY 3 | 4990 | 2992 | 1998 | 40.04%
DAY 4 | 6615 | 4009 | 2606 | 39.40%
DAY 5 | 6171 | 3682 | 2489 | 40.33%
DAY 6 | 6893 | 5067 | 1826 | 26.49%
DAY 7 | 6065 | 4112 | 1953 | 32.20%
DAY 8 | 6778 | 6011 | 767 | 11.32%
DAY 9 | 4347 | 3781 | 566 | 13.02%
DAY 10 | 4322 | 3792 | 530 | 12.26%
DAY 11 | 6575 | 5137 | 1438 | 21.87%
DAY 12 | 7516 | 5568 | 1948 | 25.92%
DAY 13 | 6053 | 4843 | 1210 | 19.99%
DAY 14 | 4719 | 4140 | 579 | 12.27%
DAY 15 | 7960 | 5897 | 2063 | 25.92%
DAY 16 | 7982 | 7002 | 980 | 12.28%
DAY 17 | 3956 | 3440 | 516 | 13.04%
DAY 18 | 8454 | 6657 | 1797 | 21.26%
DAY 19 | 4877 | 4205 | 672 | 13.78%
DAY 20 | 4950 | 3779 | 1171 | 23.66%
DAY 21 | 6160 | 5177 | 983 | 15.96%
DAY 22 | 7144 | 5332 | 1812 | 25.36%
MINIMUM | 3956 | 2992 | 516 | 11.32%
MAXIMUM | 8454 | 7002 | 2606 | 40.33%
AVERAGE | 6141 | 4760 | 1380 | 22.07%

## Slide 32: CONCLUSION
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak

## Slide 33
2022-2023 Spring - IE 4920 - Group 9 – A Warehouse Decision Support System for Totomak
System Analysis
Macro/Micro
Problem Definition
Fishbone Diagram
Modeling Approach
Tactical and Operational Level Model Formulation
Decision Support System (DSS)
Verification and Validation of the DSS
Solution Methodology
Developing the Model Base
Comparison
Conclusion

## Slide 34: Thanks!
Any questions?